ΣC2600U

Digital Speaker Management Processor

| Product Description: The ΣC2600U is a 1U integrated speaker management processor. This device is easily programmable to meet all installation applications. Key Features and Benefits: Integrated speaker management processor Three-way stereo or six-way mono crossover 32 bit floating point DSP and digital filter 2 x input XLRs + 6 x Output XLRs + 2 x RS485 XLR + USB + 1 x 6.5mm socket(BGM signal) Software programmable via PC (USB port) Provides input selection, gain control, delay, crossover, equalization and limiter functions DSP - 48kHz sample rate with 24bit AD/DA processing Front panel input and output LED indicators Store up to 20 presets Front Panel: Rear Panel: Specifications Input Connector 2 x Balanced XLR, 2 x RS485 XLR, 1 x USB + 1 x 6.5mm 6 x Balanced XLR 6 x Balanced XLR Output Connector Balanced 10kΩ Maximum Output Levels +20dBu A/D Sampling Frequency 64kHz, 24bit linear Frequency Response (±0.3dB) 20Hz-20kHz, 10Hz-30kHz THD + N <0.006% S/N Ratio (A weight) 110dB Dynamic Range ≥ 110db Power Supply 220V 50Hz Dimensions (W x D x H) 483mm (19”) x 228mm (10”) x 45mm (1.8”) Net Weight (1 piece/pack) 4.7kg (10.4lb) Gross Weight (1 piece/pack) 6.3kg (13.9lb) | Mouseover image to zoom Front View Back View |
| --- | --- |