EQ2231

Stereo Graphic Equalizer

| Product Description: The EQ2231 is a 3U 30 band, constant Q Stereo Graphic Equalizer. Key Features and Benefits: EQ filter is bypassed if fader is in centre indent position In the event of power failure a high quality relay switch sends input signal directly to output connectors Power-on delay for soft start Front Panel 2 x 30 constant Q faders ±15dB control range 9 x segment signal output LEDs Gain control High pass filter up to 250Hz Low frequency shelf filter ±6dB of gain at 50Hz High frequency shelf and filter ±6dB gain 14kHz EQ bypass switch Rear Panel 2 x Balanced XLR input connectors 2 x Balanced XLR output connectors 6.5mm inputs and outputs connectors Phoenix inputs and output connectors Front Panel: Rear Panel: Specifications Input Impedance 10kΩ Balanced and Unbalanced Overloaded Electromotive Force 8.5V Frequency Response (±1dB) 5Hz-45kHz Harmonic Distortion <0.008% THD 20-20kHz S/N Ratio >92dB Max. Output Level 9.5V Output Impedance <50Ω Dynamic Range >115dB Crosstalk >85dB @ 1kHz Frequency Control ±15dB on ISO centres Q value for 4 Power Supply 220V 50Hz Dimensions (W x D x H) 483mm (19”) x 228mm (10”) x 45mm (1.8”) Net Weight (1 piece/pack) 4.7kg (10.4lb) Gross Weight (1 piece/pack) 6.3kg (13.9lb) | Mouseover image to zoom Front View Back View |
| --- | --- |