U15

15” Two Way Full Range Plastic Speaker

| Product Description: Portable and installed plastic loudspeakers used in applications including sound reinforcement in Front of House and Foldback applications in Houses of Worship,Events, Clubs, Rehearsal Halls etc. The U Active Series delivers extraordinary performance at unmatched value. Key Features and Benefits: High output SPL and sensitivity 1 x 15” high power transducer with 50mm voice coil 1 x 1.7” diaphragm compression driver Rotatable Horn: 50º-100º x 55º controlled coverage pattern Heavy duty protective grill Injection molded 2 x NL4 connector Cabinet design for FOH and Monitor use Suitable for use as a main system with or without sub speaker augmentation Portable system (stand), or permanent installation (wall, ceiling) Arrays with all active high power U Series sub speakers for extended low frequency, high quality music reproduction Monitor kit - optional Cabinet Dimension: Specifications Construction Plastic Transducers 1 x 1.7” HF + 1 x 15”LF Frequency Response (-3dB) 40Hz-18kHz Rated Power 300W(RMS) Sensitivity (1W @ 1m) 98dB Maximum SPL (1W @ 1m) 121dB(Peak) Rated Impedance 8Ω Dispersion (H x V ) 50°-100°x55° Connector 2xNL4 Dimensions (W x D x H) 485mm(19.1”)x460mm(18.1”)x700mm(27.6”) Packaging Dimensions (1 piece/pack) 545mm(21.5”)x515mm(20.3”)x800mm(31.5”) Net Weight (1 piece/pack) 26kg(57.3lb) Gross Weight (1 piece/pack) 28kg(61.7lb) Installation drawing: | Mouseover image to zoom Relevant Download: U Series Catalog User Manual U15 Image |
| --- | --- |