U10

10” Two Way Full Range Plastic Speaker

| Product Description: Portable and installed plastic loudspeakers used in applications including sound reinforcement in Front of House and Foldback applications in Houses of Worship,Events, Clubs, Rehearsal Halls etc. The U Active Series delivers extraordinary performance at unmatched value. Key Features and Benefits: High output SPL and sensitivity 1 x 10” high power transducer with 50mm voice coil 1 x 1.3” diaphragm compression driver 90º x 60º controlled coverage pattern Rotatable Horn Heavy duty protective grill Injection molded 2 x NL4 connector Cabinet design for FOH and Monitor use Suitable for use as a main system with or without sub speaker augmentation Portable system (stand), or permanent installation (wall, ceiling, under balcony)Arrays with all active high power U Series sub speakers for extended low frequency, high quality music reproduction Monitor kit - optional Cabinet Dimension: Specifications Construction Plastic Transducers 1 x 1.3”HF+1 x 10”LF Frequency Response (-3dB) 65Hz-18kHz Rated Power 250W(RMS) Sensitivity (1W @ 1m) 95dB Maximum SPL (1W @ 1m) 119dB(Peak) Rated Impedance 8Ω Dispersion (HxV ) 90°x60° Connector 2xNL4 Dimensions (WxDxH) 321mm (12.6”) x 321mm (12.6”) x 464mm (18.3”) Dimensions (WxDxH) 375mm (14.8”) x 355mm (14”) x 535mm (21.1”) Net Weight (1 piece/pack) 10kg (22lb) Gross Weight (1 piece/pack) 12kg (26.5lb) Installation drawing: | Mouseover image to zoom Relevant Download: U Series Catalog User Manual U10 Image |
| --- | --- |